## Slide 1
FPGA DRAM Tutorial
2021.05.06 v1.0 黃家翰

## Slide 2: Outline
External Memory Interface IP
Avalon Memory-Mapped Protocol
Example Code
Quartus Project Settings
RTL Simulation with Qsys IP
Extension

## Slide 3: Outline
External Memory Interface IP
Avalon Memory-Mapped Protocol
Example Code
Quartus Project Settings
RTL Simulation with Qsys IP
Extension

## Slide 4: External Memory Interface IP
Arria 10 External Memory Interfaces (EMIF)
  這個IP可以將我們用Avalon Memory-Mapped介面傳輸的資料轉換為以DRAM介面傳輸的資料。
  由於DRAM控制較複雜，有這個IP我們就能更方便的存取DRAM中的資料。
  除了DRAM之外，這個IP也能改成與其他種類的外部記憶體溝通。 Ex. QDRII+ SRAM
Arria 10 EMIF
DRAM Protocol
Avalon Memory-Mapped Protocol
External Memory
User Logic

## Slide 5: Outline
External Memory Interface IP
Avalon Memory-Mapped Protocol
Example Code
Quartus Project Settings
RTL Simulation with Qsys IP
Extension

## Slide 6: Avalon Memory-Mapped Protocol
The Avalon Memory-Mapped interface specification is designed to accommodate peripheral development for the system-on-a-programmable-chip (SOPC) environment.
The specification provides peripheral designers with a basis for describing the address-based read/write interface found on master and slave peripherals.

## Slide 8: Avalon MM Basic Signals
Signal Type | Width | Direction | Description
address | 1-32 | M -> S | Slave address.
read | 1 | M -> S | Read-request signal to the slave port.
readdata | 1-1024 | S -> M | Data transferred from slave to master by the read operation.
write | 1 | M -> S | Write-request signal to the slave port.
writedata | 1-1024 | M -> S | Data transferred from master to slave by the write operation.
waitrequest | 1 | S -> M | Used to stall the system interconnect fabric when the slave port is not able to respond immediately.
readdatavalid | 1 | S => M | Marks the rising clock edge when the slave asserts valid readdata.

## Slide 9: Avalon MM Basic Waveform
readdatavalid

## Slide 10: Avalon MM Slave Transfer Types
Variable Latency
Fixed Latency
Pipelined Variable Latency
Pipelined Fixed Latency
Tristate
Burst
More Info:
http://www1.cs.columbia.edu/~sedwards/classes/2009/4840/mnl_avalon_spec.pdf
http://www.innovateasia.com/asia/download/document/knowledge_11_Taiwan.pdf

## Slide 11: Basic Avalon MM Operation in the example
Write:
  與SRAM操作類似。將write拉高並設定好address和writedata。但是當waitrequest訊號為1時，write、writedata、address必須保持為固定值。

## Slide 12: Basic Avalon MM Operation in the Example
Read:
  與SRAM操作類似。將read拉高並設定好address。但是當waitrequest訊號為1時，read、address必須保持為固定值。當readdatavalid訊號為1時，表示此時的readdata為有效值。

## Slide 13: Outline
External Memory Interface IP
Avalon Memory-Mapped Protocol
Example Code
Quartus Project Settings
RTL Simulation with Qsys IP
Extension

## Slide 14: Example Code
Download: https://github.com/jelly99709/FPGA-DRAM-Tutorial
Data Flow:
  Input -> Store in BRAM (A) -> Read from (A), Store in DDR4 -> Read from DDR4, Store in BRAM (B) (reversed order) -> Read from (B)-> Output
On-Chip
Block-RAM
(A)
Off-Chip
DDR4
On-Chip
Block-RAM
(B)
PCIe

## Slide 15: Example Code
Platform: DE5a-Net (with Arria 10 FPGA)
PCIe: Gen2x8 (250 MHz, 128 bit)
Lab Workstation: (Winnie)
  IP: 140.112.48.159
  Port: 40720
Prerequisites
  FPGA Riffa Tutorial https://github.com/b03901165Shih/2019-FPGA-training-course
  DE5a Riffa Settings https://github.com/jelly99709/DE5a-Riffa-Setup

## Slide 16: Example Code
Download: https://github.com/jelly99709/FPGA-DRAM-Tutorial
Data Flow:
  Input -> Store in BRAM (A) -> Read from (A), Store in DDR4 -> Read from DDR4, Store in BRAM (B) (reversed order) -> Read from (B)-> Output
On-Chip
Block-RAM
(A)
Off-Chip
DDR4
On-Chip
Block-RAM
(B)
PCIe

## Slide 17: Example Code
由於DE5a板子上DDR4記憶體的寬度為64bit，而PCIe每個週期傳輸128bit (4筆32bit的資料)。因此在此範例中為了方便起見，每筆資料僅比對低位16bit的正確性。
128 bit
128 bit
64 bit

## Slide 18: Example Code Reproduce
Copy RIFFA from workstation
  cp -r /mnt/ds1515/fpga/riffa_2.2.2/ ./
Open project directory DE5Gen2x8If128
  Located at ./riffa_2.2.2/source/fpga/altera/de5/
Copy files under Quartus_Project into their corresponding folders
  *.qpf, *.qsf -> prj
  *.sdc -> constr
  *.v -> hdl
  *.qsys -> ip
Copy files under test_DRAM into their corresponding folders.
  *.v -> ./riffa_2.2.2/source/fpga/riffa_hdl/
  sample_app -> ./riffa_2.2.2/source/c_c++/linux/x64/

## Slide 19: Example Code Reproduce
Open project in Quartus
Open Qsys IP files and generate HDL (兩個IP都要)
  Open Qsys tool
  File -> Open -> ../ip/QsysDE5Gen2x8If128.qsys or ../ip/QsysDDR4.qsys
  Generate -> Generate HDL
Check user-define SDC in the last order
  Quartus -> Assignments -> TimeQuest Timing Analyzer
Compile and Program Device
Reboot Computer and Test

## Slide 20: Outline
External Memory Interface IP
Avalon Memory-Mapped Protocol
Example Code
Quartus Project Settings
RTL Simulation with Qsys IP
Extension

## Slide 21: Quartus Project Settings
Check the user manual and example projects in the CD-ROM for more information
  DE5: https://www.terasic.com.tw/cgi-bin/page/archive.pl?Language=Taiwan&CategoryNo=159&No=726&PartNo=4
  DE5a: https://www.terasic.com.tw/cgi-bin/page/archive.pl?Language=Taiwan&CategoryNo=2&No=1138&PartNo=4
Assignment Settings File
  Add DDR4 and RZQ pin assignments to the *.qsf file

## Slide 22: DDR4 Qsys IP Design
Arria 10 EMIF
Clock-Crossing Bridge
DDR4 Protocol
Pipeline Bridge
AMM
AMM
To user logic
AMM
To DDR
(300 MHz)
(300 MHz)
(300 MHz) (user clk)
(user clk)
外部記憶體控制IP
避免EMIF和clock-crossing bridge中間有timing violation。但會使latency增加。可省略。
處理跨越不同clock domain的AMM訊號

## Slide 23: DDR4 Qsys IP Design
如右圖設定IP連線與對外接腳
個別IP參數設定請參考IP_Settings資料夾 (clk、pipelining、burst、FIFO可視需求更改)
EMIF參數設定與DE5a上裝置之DDR有關，請勿任意更改。
完成後點選generate HDL

## Slide 24: Quartus Top Module
新增對外DDR pin。
新增DDR4 IP instance與對應接腳。
Reset訊號是active low，與riffa reset反相。
新增chnl_tester與DDR4 IP的接口
EMIF校正狀態訊號 只有剛啟動時會出現 當success非1時 不能以AMM與EMIF溝通
※ 具體設置請參考example code

## Slide 25: SDC File
EMIF IP status signals to user logic and clock-crossing bridge (EMIF校正狀態訊號並未經過clock-crossing處理，且僅初始化時變動，故設false path)
RIFFA reset signal to Altera EMIF IP (recover time violation) (EMIF內部有reset synchronizer，故可忽略input async reset的recover time violation)

## Slide 26: Timing
Compile完在EMIF內部仍有timing violation。但這結果與terasic提供之範例程式結果相似，故暫時忽略。

## Slide 27: Outline
External Memory Interface IP
Avalon Memory-Mapped Protocol
Example Code
Quartus Project Settings
RTL Simulation with Qsys IP
Extension

## Slide 28: RTL simulation with Qsys IP
Simulation using NCVerilog
  cd (Qsys Path)/(IP Name)/sim/cadence/
  setenv CDS_ROOT “/cad/cadence/INCISIV/cur/”
  bash ncsim_setup.sh SKIP_ELAB=1 SKIP_SIM=1
  cp <design and testbench files> ./
  ncverilog <testbench_files> <design_files> +access+r

## Slide 29
External Memory Pins
Simulation Memory IP Selection - 1
Altera EMIF IP
  Need external memory pins.
  DE5a-Net uses Micron DDR4 SODIMM 64x 4GB Memory.
  However, Micorn dose not provide verilog simulation model for SODIMM.

## Slide 30
Simulation Memory IP Selection - 2
Altera On-Chip Memory IP
  No external pin connection.
  Limited memory size (<64Mbit)
See ./Simulation/IPtest.qsys for more information

## Slide 31
Simulation Memory IP Selection - 3
Hand-crafted Avalon MM Slave Model
  See ./Simulation/amm_slave.v for more information (A simple amm slave model in the variable latency transfer mode)

## Slide 32: Memory IP Simulation Example Code
To run the example code in ./Simulation folder:
  Open IPtest.qsys in Qsys tool and gerenate HDL with simulation code.
  Follow the instructions in page 28
Data Flow
On-Chip
Block-RAM
Model
Memory IP Simulation Model
On-Chip
Block-RAM
Model
Testbench

## Slide 33: Outline
External Memory Interface IP
Avalon Memory-Mapped Protocol
Example Code
Quartus Project Settings
RTL Simulation with Qsys IP
Extension

## Slide 34: Extension
Directly Data Transmission between Riffa and DRAM
RTL Simulation with Qsys IP and SODIMM Model
RTL Simulation with hand-crafted full-function amm slave model
Low-Latency DDR Access
  Avalon-MM Burst Mode
  Avalon-MM DDR Memory Half-Rate Bridge
Timing Violation

## Slide 35: Appendix
DDR3 SDRAM Controller with UniPHY
  使用在DE5板子(Stratix V FPGA)上時所需的IP，與EMIF的功能大同小異。
  IP參數設定與pin assignment請參考附件DRAM_DE5.zip
SDRAM Control
DDR3 Protocol
Avalon Memory-Mapped Protocol
DDR3
Memory
User Logic